## Slide 1
⚡ TELECOM DIGITAL TWIN ARCHITECTURE
Digital Twin Adapters & Standards
How Intent, ETSI TeraFlowSDN, NS-3 Co-Simulation, and Ceragon Microwave Hardware Interconnect
• What are the Adapters? Software translators bridging heterogeneous timing, data formats, and control protocols.
• International Standards: Anchored in TM Forum TMF921, 3GPP TS 28.561, ITU-T Y.3090, IETF DTI, and RFC 8040 RESTCONF.
• Closed-Loop Automation: Zero-risk What-If discrete prediction prior to physical hardware 2-phase commit actuation.
Ceragon Networks & ETSI TeraFlowSDN Research • Standalone & Production Hybrid Architecture

## Slide 2
THE PROBLEM & ARCHITECTURAL NEED
The Core Problem: Why Do We Need Adapters?
💡 In a Telecom Digital Twin, components speak completely different languages and operate at vastly different timescales. Adapters are the critical translators that bridge this semantic and temporal chasm.
1. Declarative Intent
Human Operator / SLA
Speaks: Natural Language / JSON
Timescale: Minutes to Days
Key Data: "Ensure URLLC latency < 1.5ms and 99.999% availability during storms"
2. SDN Controller
ETSI TeraFlowSDN
Speaks: Context DB, gRPC, CSPF
Timescale: Seconds (Control Plane)
Key Data: Device UUIDs, Endpoints, Topology Graphs, TI-LFA backup paths
3. Discrete Simulator
NS-3 Discrete Core
Speaks: C++ Event Queue & Packets
Timescale: Microseconds (t = 0.000s)
Key Data: QueueDisc buffer drops, WiFi EDCA AC_VO, link propagation delay
4. Physical Hardware
Ceragon MH-T261
Speaks: RFC 8040 RESTCONF & PHY
Timescale: Sub-millisecond Hardware
Key Data: V-Band 60.48 GHz, ACM MCS 0-9, PHY RSSI/SNR, RF registers

## Slide 3
INTERNATIONAL STANDARDS REFERENCE
Standards for Digital Twin APIs We Use & What They Are
TM Forum TMF921 [BUSINESS & SLA]
Intent Management API
Standard: REST API standard for expressing declarative network intent and SLA expectations.
In Our Platform: Operator defines latency (< 1.5ms) and availability without writing low-level scripts. Tracks intent state: Acknowledged → In Evaluation → Compliant.
3GPP TS 28.561 [5G / 6G CORE]
Network Digital Twin (NDT) Lifecycle
Standard: 3GPP 5G/6G standard defining digital twin management services and closed-loop control.
In Our Platform: Governs the 4-phase pre-flight verification gate before any action is actuated: verifies latency envelope, queue stability, jitter, and spectral mask.
ITU-T Y.3090 [ARCHITECTURE]
Digital Twin Network (DTN) Architecture
Standard: ITU-T standard defining the 3-layer Digital Twin reference model and synchronization.
In Our Platform: Defines data repository synchronization between the Physical Network Layer and the Cyber Twin Layer. Powers our real-time shadow datastore.
IETF NMRG DTI [SIMULATION SBI]
Digital Twin Interface (RFC Draft)
Standard: IETF Network Management Research Group interface for Twin-to-Simulator communication.
In Our Platform: Standardizes the East-West protocol for injecting What-If perturbations (traffic surge, rain fade) and streaming discrete telemetry back to controller.
IETF RFC 8040 / 7950 [HARDWARE SBI]
RESTCONF Protocol & YANG 1.1
Standard: IETF standard for HTTP-based network device management accessing YANG data stores.
In Our Platform: Southbound interface to Ceragon MH-T261 (192.168.1.225:80). Provides Candidate Datastore staging, diff validation, and 2-Phase Commit (2PC).
ETSI TeraFlowSDN APIs [SDN CONTROL]
Cloud-Native SDN Controller Microservices
Standard: ETSI standard cloud-native gRPC microservices pipeline for autonomous transport networks.
In Our Platform: Exposes Context Service (gRPC :10010), Service/PCE (gRPC :10030), Device Driver (gRPC :10020), and Monitoring Telemetry Daemon (gRPC :10040).

## Slide 4
HOW THE ADAPTER FUNCTIONS
Adapter 1: TFS-to-NS-3 Simulation Adapter (The Cyber Mirror)
🔁 Step-by-Step Functional Flow (Simplified)
Step 1: Reconcile Live Topology & State The adapter queries ETSI TeraFlowSDN (:8088 Context) to extract the active 34-node graph, link bandwidths, and live Ceragon RF metrics (RSSI -58 dBm, MCS 8).
Step 2: Simulation Resolution Governor (Fidelity Scoping) Instead of simulating all 34 nodes (which takes minutes), the Governor automatically scopes the graph to the relevant target domain (e.g. Tier 4: URLLC Micro-Packet, 23 nodes) executing in ~1150ms.
Step 3: What-If Perturbation Dispatch Injects real-world stress conditions into NS-3: 3.5x bulk traffic surge (bufferbloat) or ITU-R P.838 rain fade (ACM rate degradation from 1Gbps to 100Mbps).
Step 4: Discrete Trace Ingestion & NetAnim Generation NS-3 simulates microsecond discrete packet events on cersrv-029, generates /tmp/tsn_wifi_ceragon_anim.xml, and the adapter streams packet queues, buffer drops, and latencies back to the twin.
⚙️ Key Implementation Features
• Remote Execution Core: Dispatches via SSH/JSON to ns-3.45 on efid@cersrv-029; falls back to analytical local simulation for zero-dependency standalone mode.
• Multi-Tier Governor: 5 Resolution Tiers (Macro-Topology 25%, Queue Dynamics 55%, Physical RF 75%, URLLC 95%, Green Energy 20%).
• NetAnim XML Output: Instruments AnimationInterface for real timeline playback (0.000s - 2.500s) with 10 visual buffer slots and tail-drop alerts.
• Deterministic TSN Mapping: Maps 802.1Q PCP Class 6 & EDCA AC_VO into PfifoFast Band 0 priority queues.

## Slide 5
PHYSICAL ACTUATION & TELEMETRY
Adapter 2: TFS Southbound & Hardware Driver Adapter
📝 STAGE 1
Candidate Datastore Staging
Translates AI Decision Engine output into concrete YANG configuration rules staged in ETSI TeraFlowSDN's Candidate Datastore (RFC 8040).
• Target Device: Ceragon MH-T261 (UUID f676623c...)
• ACM Floor Hardened: MCS 0 → MCS 4 (≥ 500 Mbps min)
• QoS Queue: FIFO → IEEE 802.1Q PCP Class 6 (PfifoFast)
• Carrier Frequency: 60.48 GHz → 64.80 GHz
🛡️ STAGE 2
Pre-Flight Safety Envelope Gate
Before touching physical production traffic, 3GPP TS 28.561 requires verification of the candidate configuration against live constraints.
• Gate 1: Latency Bound Pass (Predicted 1.12ms ≤ 1.5ms)
• Gate 2: Queue Stability Pass (Buffer occupancy < 40%)
• Gate 3: Hardware Capability Pass (MH-T261 supports MCS 4)
• Gate 4: Spectral Mask Pass (64.80 GHz approved in V-Band)
🚀 STAGE 3
RFC 8040 RESTCONF 2PC Commit
Executes Two-Phase Commit transaction directly over HTTP/RESTCONF to physical transceiver socket 192.168.1.225:80.
• Phase 1 (Prepare): PATCH candidate datastore via RESTCONF
• Phase 2 (Commit): POST ietf-netconf:commit operation
• Telemetry Verification: Continuous RFC 8040 poll
• Instant Rollback: Automatic 2PC revert if health checks fail
🔒 Zero-Outage Guarantee: By combining Candidate Datastore staging, Pre-Flight discrete validation, and 2-Phase Commit, the adapter ensures that bad configurations are rejected in software before they can impact customer SLA.

## Slide 6
ARCHITECTURE SUMMARY
Summary: End-to-End Closed-Loop Operational Value
🛡️ Zero-Risk What-If Validation
Predictive Discrete Simulation
Operators can test severe perturbations (3.5x bulk surges, category-5 tropical rain fade, fiber link cuts) in a microsecond-accurate digital twin without putting live production circuits at risk.
🌐 Standardized Multi-Vendor Interoperability
Anchored in 3GPP, ITU-T & IETF
Zero proprietary lock-in. Built entirely on open telecom specifications: TM Forum TMF921 Intent API, 3GPP TS 28.561 NDT lifecycle, ITU-T Y.3090, IETF DTI, and RFC 8040 RESTCONF.
⚡ Sub-Second Autonomous Closed Loop
Autonomous Self-Healing Transport
Replaces hours of manual CLI troubleshooting with autonomous, closed-loop assurance: SLA intent is ingested, simulated in NS-3, safety-verified, and actuated via TFS in ~1.9 to 2.2 seconds total.
📋 Digital Twin Adapter Quick Reference Table
• Intent Adapter: Translates Natural Language / SLA bounds into TFS Service & CSPF requests (TM Forum TMF921).
• Simulation Adapter: Syncs TFS live graph into NS-3 C++ discrete engine, scopes fidelity (Tiers 1-5), and outputs microsecond traces.
• Southbound Driver: Manages candidate datastore diffs and 2-phase commits to Ceragon MH-T261 via RFC 8040 RESTCONF.